## Slide 1: Faster tests, greener cars
How machine learning can help plan the end-of-line test bench
Mohammad Bajbouj · ML project (Kaggle: Mercedes-Benz Greener Manufacturing) · neuefische AI PM bootcamp · October 2026
© 2026 Mohammad Bajbouj. All rights reserved. Decisions by Mohammad Bajbouj; drafted with Claude by Anthropic (Cowork, Claude Code); winner research drafted by Gemini (Google). Practice project, neuefische AI PM bootcamp. Kaggle data (Mercedes-Benz) is not covered by this copyright notice.
Notes: Welcome. Every new Mercedes-Benz car is tested on a test bench before delivery, and the time each car needs differs. I will show how machine learning can predict that time, how well it works, and what it could mean for planning and energy use.

## Slide 2: The challenge
Main
Unique
almost every car is configured differently
Every car
is tested on a test bench before delivery
72–265 s
test times differ from car to car – hard to plan the bench
Meaning: if we knew each car's test time in advance, we could plan the test bench better – less waiting, less energy.
Notes: Almost every car leaves the factory with its own configuration. Every car is tested before delivery, and the test takes between 72 and 265 seconds. Because the time differs from car to car, the test bench is hard to plan. If we knew each car's time in advance, we could plan better – less waiting, less energy.

## Slide 3: Our hypothesis
Main
Hypothesis (H2): Does the same car configuration always need the same test time?
1
Why it matters: if not, part of the test time can never be predicted from the configuration
2
Our approach: compare cars with identical configurations, then predict with three different machine-learning methods
3
Where we answer the hypothesis: slide 5 (identical cars) and slide 7 (three methods)
Notes: Our hypothesis, H2: does the same car configuration always need the same test time? If yes, the configuration tells us the time exactly. If no, part of the time comes from the test itself, and nobody can predict that part. We checked this with real data and three different machine-learning methods.

## Slide 4: What we worked with
Main
4,209
tested Mercedes-Benz cars (public Kaggle data)
376
columns per car – Mercedes-Benz hid the real names of the 376 columns
Seconds
one measured test time per car – what we predict
Meaning: real factory data, but anonymised: we see the values, not what each column means (→ slide 14).
→ explained on slide 14
Notes: We worked with real, public factory data from a Kaggle competition by Mercedes-Benz: 4,209 tested cars. Each car is described by 376 columns, but the real names of the columns are hidden. For each car we know one measured test time – that is what we predict.

## Slide 5: Finding 1: same car, different time
Main
Cars with exactly the same configuration still need different test times – by about 8 seconds.
≈ 60 %
of the differences in test time between different cars can be predicted, using the configuration as indicator – at most
≈ 40 %
comes from the test itself (e.g. human error) – no model can predict it
Meaning: the answer to our hypothesis is no – and this sets a clear limit for any prediction (→ slide 15).
→ explained on slides 15–16
Notes: Our first finding: cars with exactly the same configuration still need different test times, by about 8 seconds. Using the configuration as indicator, we can predict up to about 60 % of the differences in test time between different cars. The other 40 % come from the test itself – for example human error, which the data does not record. So the answer to our hypothesis is no, and this sets a clear limit.

## Slide 6: Finding 2: one column tells most of the story
Main
Each car is described by 376 columns. One column, X0, sorts the cars into a few typical test times.
57.5 %
of the differences in test time between cars are explained by the column X0 alone
375
the other 375 columns mostly repeat what X0 already says
Meaning: the test time depends mainly on the value in one column, X0 (→ slide 17).
→ explained on slide 17
Notes: Our second finding: each car is described by 376 columns, and one column, X0, sorts the cars into a few typical test times. X0 alone explains 57.5 % of the differences in test time between cars. The other 375 columns mostly repeat what X0 already says.

## Slide 7: Our prediction
Main
Without a model
± 12.4 s
typical planning error if every car gets the same average time
With our model
± 8.0 s
about 4.5 s closer per car – already at the limit set by the test itself
Meaning: the average test time is about 100.6 s. Without a model the plan is off by about 12.4 s per car, with our model by about 8 s. Three different methods all landed here, so we keep the simplest (→ slide 18).
→ explained on slide 18
Notes: The average test time is about 100.6 seconds. If we plan every car with this same average, the plan is off by about 12.4 seconds per car. With our model it is off by about 8 seconds – about 4.5 seconds closer per car. That is already at the limit set by the test itself, and three very different methods all landed there.

## Slide 8: How good is it?
Main
91 of 100
cars predicted within 10 seconds (tested on cars the model had not seen)
97 %
of the Kaggle winner's score (score = share of the differences explained), with one column (X0)
A few
very long tests are the big misses – they come from the test itself
Meaning: accurate enough to plan a test bench – not to promise each single car's time (→ slide 19).
→ explained on slide 19
Notes: How good is it? For 91 of 100 cars the prediction is within 10 seconds – tested on cars the model had never seen. In the official Kaggle check we reach 97 % of the competition winner's score, using only one column, X0. The big misses are a few very long tests that come from the test itself.

## Slide 9: What it means for planning
Main
Car order
its configuration is known in advance
Prediction
expected test time for this car
Bench plan
a slot per car + a buffer for unusual tests
Expert view (Mohammad Bajbouj, automotive R&D): plan each car with its predicted test time to reduce energy use in the end, and keep a buffer for extraordinary test times.
The test itself does not get shorter – the plan gets more accurate: less waiting and less overrun on the bench.
Notes: What does this mean for planning? The car order brings its configuration, the model predicts the expected test time, and the bench plan gets a slot per car plus a buffer for unusual tests. My view from automotive R&D: plan each car with its predicted time to reduce energy use, and keep a buffer for extraordinary test times. The test itself does not get shorter – the plan gets more accurate.

## Slide 10: Why it matters at factory scale
Main
≈ 1,300
cars a day in one large plant (about 300,000 a year)
4.5 s
more accurate plan per car
≈ 1.6 h
of more accurate bench planning every day – not shorter tests
Meaning: small per car, large per day – the energy saving is a hypothesis we propose to test in a pilot (→ slide 20).
→ explained on slide 20
Notes: Why does this matter? A large plant like Sindelfingen built about 300,000 cars a year, roughly 1,300 a day. 4.5 seconds per car add up to about 1.6 hours of more accurate bench planning every day – not shorter tests. Whether this saves energy is a hypothesis we propose to test in a pilot.

## Slide 11: Next steps
Main
Pilot
one test bench, one day, then one month: measure idle time and energy before and after planning with predictions
Record more
long tests cannot be predicted from the configuration – record bench, tester and day to explain them (→ slide 21)
Know the limits
about 60 % is the limit; plan with predictions, don't promise single cars
→ explained on slide 21
Notes: Three next steps. First, a pilot on one test bench – one day, then one month – measuring idle time and energy before and after. Second, record more about each test run, because long tests cannot be predicted from the configuration. Third, keep the limit in mind: about 60 % is the most that can be predicted.

## Slide 12: Key takeaways
Main
1
Even identical cars need different test times – at most about 60 % of the differences in test time between cars can be predicted
2
One column, X0, explains almost all of that predictable part
3
Our model plans each car about 4.5 seconds more accurately – 91 of 100 cars within 10 seconds
4
At factory scale this means about 1.6 hours of better planning per day – a pilot can show the energy saving
Meaning: the data, not the choice of method, sets the limit – and we already reach it.
Notes: To sum up: even identical cars need different test times, so at most about 60 % of the differences in test time between cars can be predicted. One column, X0, explains almost all of that. Our model plans each car about 4.5 seconds more accurately, and at factory scale that is about 1.6 hours of better planning per day. The data, not the method, sets the limit – and we already reach it.

## Slide 13: Explanation slides
For questions. Each slide names the main slide it belongs to.
Notes: Explanation slides – used only when questions come up. Each one links back to its main slide.

## Slide 14: Where the data comes from
Explain
1
Public Kaggle competition by Mercedes-Benz ("Greener Manufacturing", 2017): 4,209 tested cars with their measured test time
2
376 columns per car: 8 text columns (e.g. X0) and 368 yes/no columns – the real names of the columns are hidden
3
Test times from 72.11 s to 265.32 s; one 265 s test looked faulty and was left out of training
4
A second set of 4,209 cars without test times is used by Kaggle to check every model fairly
→ belongs to main slide 4
Notes: The data is public: a Kaggle competition Mercedes-Benz ran in 2017. 4,209 cars with test times, 376 hidden columns each, and a second set of 4,209 cars that Kaggle uses to check every model fairly.

## Slide 15: How we found identical cars
Explain
1
We compared all 376 columns of every car: 515 of 4,209 cars have at least one identical twin (217 groups)
2
Example: 9 identical cars needed between 106 and 128 seconds – up to 22 seconds apart
3
Across all groups, identical cars differ by about 8 seconds – this part is noise from the test itself
4
A person can check every group by hand; the twins behave like all other cars
→ belongs to main slide 5
Notes: We compared all 376 columns of every car and found 515 cars with an identical twin. The largest group – 9 identical cars – needed between 106 and 128 seconds. Across all groups, identical cars differ by about 8 seconds.

## Slide 16: Where the 60 % comes from
Explain
1
All cars together: test times spread about 12.7 seconds around the average of 100.7 seconds
2
Identical cars: still about 8.1 seconds apart – the configuration is the same, so this cannot come from it
3
Comparing the two spreads: about 40 % of the differences is noise, so at most about 60 % can be predicted
4
The calculation step by step is in the engineering deck (slides 22–23)
→ belongs to main slide 5
Notes: All cars spread about 12.7 seconds around the average; identical cars still about 8.1 seconds. Comparing the two spreads shows that about 40 % of the differences is noise. So at most about 60 % can be predicted.

## Slide 17: What X0 is
Explain
1
X0 is not a method – it is one column of the data; every car has one of 47 X0 values
2
Cars with the same X0 value have similar test times (e.g. groups around 75, 90, 100 or 108 seconds)
3
We cleaned the data: 66 columns never change or copy another column → 310 columns left
4
Adding these 310 columns did not improve the prediction – the 310 columns repeat what X0 already says
→ belongs to main slide 6
Notes: X0 is one column, not a method. Every car has one of 47 X0 values, and cars with the same X0 value have similar test times. The other columns mostly repeat what X0 says, so adding the other columns did not help.

## Slide 18: Three methods, one result
Explain
1
Ridge: one straight-line formula – it cannot see combinations of columns. Random Forest: many decision trees, averaged – it can catch combinations Ridge misses. XGBoost: trees that fix each other's errors – usually the strongest for data like ours
2
Fair test: each method learned from part of the cars and was checked on cars it had not seen, in 5 rounds
3
All three: about 8 seconds typical error, about 59 % of the differences explained – equal
4
The stronger methods found nothing extra – so the limit is in the data, not in the method, and we keep the simplest: Ridge with X0
→ belongs to main slide 7
Notes: We used three very different methods on purpose. Ridge is one straight-line formula and cannot see combinations of columns; Random Forest averages many decision trees and can catch combinations; XGBoost builds trees that correct each other and is usually the strongest for data like ours. All three ended at the same result, so the limit is in the data and we keep the simplest.

## Slide 19: What the scores mean
Explain
1
"Explained" = how much of the differences between cars the model can account for – not an error rate
2
Kaggle check on 4,209 hidden cars: our model 54.1 %, competition winner 55.6 %, limit about 59.7 %
3
So we reach 97 % of the winner's score and 91 % of what is possible – with one column (X0)
4
91 of 100 cars are predicted within 10 seconds; the big misses are a few very long tests
→ belongs to main slide 8
Notes: "Explained" means how much of the differences between cars the model accounts for – it is not an error rate. On Kaggle's hidden cars our model explains 54.1 %, the winner 55.6 %, and the limit is about 59.7 %.

## Slide 20: The factory-scale estimate
Explain
1
Production: the Sindelfingen plant built more than 300,000 cars in 2017 (Wikipedia) – the year of the Kaggle data
2
Per day: about 1,300 cars, assuming about 230 working days (our assumption)
3
4.5 seconds more accurate per car × 1,300 cars ≈ 5,850 seconds ≈ 1.6 hours of better planning per day
4
Energy saving is a hypothesis: the data has no energy values, and we don't know which plant the data comes from
→ belongs to main slide 10
Notes: The Sindelfingen plant built more than 300,000 cars in 2017. With about 230 working days – our assumption – that is about 1,300 cars a day. 4.5 seconds times 1,300 cars is about 1.6 hours of better planning per day; the energy effect still has to be measured.

## Slide 21: Why long tests cannot be predicted
Explain
1
50 of 4,209 tests took unusually long (over 136 seconds)
2
Identical twins of these cars ran normally – in all 9 cases
3
The best warning rule is right for only 1 in 39 flagged cars – about twice as good as chance
4
So the extra time comes from the test run (bench, tester, day) → future work: record these data and test a targeted buffer
→ belongs to main slide 11
Notes: 50 of 4,209 tests took unusually long. Identical twins of these cars ran normally in all 9 cases, and the best warning rule is right for only 1 in 39 flagged cars. So the extra time comes from the test run itself – that is why we propose recording test-run data.